## Slide 1: Computer Architecture Concepts
Part 1 – Logic gates

## Slide 2: Objectives
Introduce the following concepts:
  Binary data
  Logic gates
  Truth tables

## Slide 3: Binary data and logic gates
Electrical signals in computers are considered to be in one of two possible states
  High / Low
  On / Off
  True (t) / False (f)
  1 / 0
As there are two states, this is binary
We can combine binary information using Boolean logic – using logic gates
1
0
OR
1
0
OR

## Slide 4: AND Gate
A | B | X
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
Boolean Notation : X = A . B
or
X = AB
The AND gate outputs 1 when all the inputs are 1
( X = 1 when both A AND B are 1 )
Symbol
Truth table
Shows the output X for all possible inputs

## Slide 5: OR Gate
Boolean Notation : X = A + B
A | B | X
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
The OR gate outputs a 1 when either OR both of the inputs is a 1
(X = 1 if A OR B = 1, OR both).

## Slide 6: NOT Gate
A | X
0 | 1
1 | 0
Boolean Notation : X =
The NOT gate outputs a 1 when the input is 0 and outputs a 0 when the input is 1.
The NOT gate is also referred to as an inverter, as it inverts its input

## Slide 7: NAND Gate
A | B | X
0 | 0 | 
0 | 1 | 
1 | 0 | 
1 | 1 | 
1
1
1
0
Boolean Notation : X =
or X =
The NAND gate behaves like an AND gate whose output is then passed through a NOT gate
Thus NOT AND is shortened to give NAND
  Therefore the truth table is the opposite of an AND gate

## Slide 8: NOR Gate
Boolean Notation : X =
A | B | X
0 | 0 | 
0 | 1 | 
1 | 0 | 
1 | 1 | 
1
0
0
0
The NOR gate behaves like an OR gate whose output is then passed through a NOT gate
Thus NOT OR is shortened to give NOR
  Therefore the truth table is the opposite of an OR gate

## Slide 9: XOR Gate
Boolean Notation : X = A ⊕ B
A | B | X
0 | 0 | 
0 | 1 | 
1 | 0 | 
1 | 1 | 
0
1
1
0
The XOR gate (exclusive OR) outputs 1 when only one of its inputs is a 1
  X = 1 if A OR B = 1, but not both
The XOR gate outputs 0 when both inputs are the same as each other, and outputs 1 when the inputs are different

## Slide 10: Multiple Inputs
Each logic gate can have only one output, but any number of inputs
  Except the NOT gate which can only have one input
The number of rows in the truth table depends on the number of inputs to the gate
  number of rows = 2n (where n is the number of inputs)
The example shows a three input OR gate
  The truth table has 23 (2 x 2 x 2 = 8) rows
A | B | C | X
0 | 0 | 0 | 
0 | 0 | 1 | 
0 | 1 | 0 | 
0 | 1 | 1 | 
1 | 0 | 0 | 
1 | 0 | 1 | 
1 | 1 | 0 | 
1 | 1 | 1 | 
0
1
1
1
1
1
1
1

## Slide 11: Summary
AND OR NOT
NAND NOR XOR