## Slide 1: Computer Architecture Concepts
Part 8 – Representing negative integers

## Slide 2: Objectives
To introduce the two’s complement approach to storing negative numbers in binary

## Slide 3: Two’s complement
To express a value in two’s complement:
  If the number is positive (or zero), just convert it to binary and you’re done.
  If the number is negative, work out the binary of the positive value, invert each of the bits and then add 1
Notes:
  When the highest order bit is negative, the number is negative
  The number of bits being used for the representation is important
  In practice, all modern computers use 2’s complement.

## Slide 4: Two’s complement examples
To get the binary for -27 in 8-bit two’s complement
  Work out the binary for +27 00011011
  Invert all the bits 11100100
  Add 1 to give the representation for -27 11100101
To get the binary for -3 in 8-bit two’s complement
  Work out the binary for +3 00000011
  Invert all the bits 11111100
  Add 1 to give the representation for -3 11111101

## Slide 5: Two’s complement examples binary to decimal
To get the decimal equivalent of 11110010 which represents a number in 8-bit two’s complement
The most significant bit is a 1, so we know it’s a negative number
  Flip all bits 00001101
  Add 1 00001110
  Convert 1110 to decimal – gives 14
The original number 11110010 was -14

## Slide 6: Two’s complement - range
Using 4-bit representation
  All possible binary values are 0000 … 1111
  Remember that gives us 16 different values
All numbers starting with 1 are negative
All the positive numbers we can make are
  000 to 111 (that is 0 to 7 in decimal)
All the negative numbers we can make are
  1000 to 1111 (-8 to -1 respectively in decimal)
We have 16 different values from decimal -8 to +7

## Slide 7: Two’s complement - range
Using 8-bit representation
  Range -128 to 127
Note
  Decimal 127 is 01111111
  Adding 1 gives 10000000, but this represents -128

## Slide 8: Subtraction by adding a negative
Suppose we want to work out the decimal calculation 15 – 4
We can treat it as 15 + (-4)
Using 8-bit two’s complement
15 is binary 00001111, +4 is binary 00000100
Twos complement of 00000100
  Invert gives 11111011
  Add 1 11111100
Add the two numbers and ignore the overflow:
  00001111
  11111100 +
  ---------
  00001011
Convert back to decimal to check
  Binary 1011 is decimal 11

## Slide 9: Subtraction by adding a negative – example 2
Suppose we want to work out the decimal calculation 48 - 19
We can treat it as 48 + (-19)
Using 8-bit two’s complement
48 is binary 00110000
+19 is binary 00010011
Twos complement of 00010011
  Invert gives 11101100
  Add 1 11101101
Add the two numbers and ignore the overflow:
  00110000
  11101101 +
  ---------
  00011101
Convert back to decimal to check
  Binary 11101 is decimal 29

## Slide 10: Beware the overflow
Using two’s complement addition, if we add two numbers of the same sign (both positive or both negative) and the sign of the result is different then overflow has occurred
Example:
  Using 8-bit two’s complement binary arithmetic, find the sum of 107 and 46.
  Decimal 107 is 01101011
  Decimal 46 is 00101110
  Binary addition gives 10011001
    This has a 1 in the most significant bit and so represents a negative number so the answer is wrong
We see that the nonzero carry from the seventh bit overflows into the sign bit, giving us the erroneous result: 107 + 46 = -103.

## Slide 11: Summary
Two’s complement is the most widely used method for representing signed integers in binary
To convert between binary and decimal we need a number of steps
  Work out the binary for positive value
  Invert all the bits
  Add 1 to give the representation for the negative value