## Slide 1: Computer Architecture Concepts
Part 13 – Registers and memory

## Slide 2: Objectives
To describe the concept of a register and consider how one could be constructed from flip-flops
Describe addressable memory and see how it could be constructed from registers

## Slide 3: Flip-flop
A flip-flop can store and output one bit of data
Changes to the flip-flop happen on the rising-edge of the clock signal
  The clock signal is input at the point that has the triangle symbol

## Slide 4: Register
We can group flip-flops together to store more bits
This storage is called a register
Note that they all have the same clock signal so the storage is synchronised
A CPU contains registers

## Slide 5: Register in Logisim
The register has several inputs
  D for data to store
  Q for output
  Clock
  Enable – the value stored will only change when the clock changes to 1 and the Enable signal is 1
  Zero – to set the register back to storing zero
  This register stores 8 bits – so is shown as storing two hex digits (00)

## Slide 6: Memory
A register is a collection of bits
We need to consider how we could use many registers in a system
We assign each register a number
  This number is the address
  Addresses generally start at 0 and go up in ones
We need to make sure that only the one we want is updated
  We can feed the address signal to a decoder and connect the decoder’s outputs to the enable inputs of the registers so that only one register has enable set to 1
We need to be able to read the output from a specific register
  We can use a multiplexer (selector) to select the required register according to an address signal

## Slide 7: Summary
We have seen how flip-flops can be connected together to form a register
We have considered how we might use many registers together with an address to specify which one to use to form addressable memory