## Slide 1: Computer Architecture
Lectorial Week 4

## Slide 2: Objectives
Looking at last week’s reinforcement exercises
  Counter
  Memory (RAM)
Looking forward
  What is a program?
  Combining parts we have made to automate a sequence of instructions

## Slide 3: Week 3 Reinforcement Part 2
Create a 3-bit counter
  Use Logisim built-in D flip-flop
  Add ability to reset to zero and to set a specific value
Decimal | 4 | 2 | 1
0 | 0 | 0 | 0
1 | 0 | 0 | 1
2 | 0 | 1 | 0
3 | 0 | 1 | 1
4 | 1 | 0 | 0
5 | 1 | 0 | 1
6 | 1 | 1 | 0
7 | 1 | 1 | 1

## Slide 4: Week 3 Reinforcement Part 2
Create a counter using Logisim inbuilt flip-flops
Combining the outputs to an output pin

## Slide 5: Counter
Clicking the clock to increment

## Slide 6: Counter with reset button
Before reset
After reset

## Slide 7: Counter with set and reset
Want to set the counter to a specified value
Use a 3-bit input pin for the value and a 1-bit input to indicate that the value needs to be used
Need to use both the 1 and 0 inputs on the flip-flop
Want to set the 1 input to 1 when
  Corresponding bit on input pin is 1
  AND
  Set button is pressed

## Slide 8: Counter with set and reset
Here you have to do reset before set

## Slide 9: Counter with set and reset
Additional gates so that set works fully without pressing reset first

## Slide 10: Week 3 Reinforcement Part 3
Addressable Memory
  In the lab we looked at ROM
    Set the values stored in four registers manually (4-bit data)
    Used a multiplexer to select the data from a specific 2-bit address
  Now we need to look at being able to update the data in the memory – RAM
    Set the value in the register at a specific address from an input pin
    Keep the part that selects the data from the required register
Investigating the Logisim built-in memory components

## Slide 11: Creating RAM
How to store a value?
Have a 4-bit input
  Can connect this to the data (D) input on the registers
Have to only update the register at the address given
  Can set the enable input to 1 only for the register we want to update
  Can use a decoder to decode the address and pass a signal of 1

## Slide 12: Creating RAM
4-bit input data
2-bit address
  Four registers – each holds 4-bits
  Addresses are 0 to 3 in decimal
Store signal for storing the input according to the address
4-bit output data

## Slide 13: Storing a value in the RAM
I want to store decimal 12 (binary 1100, or hex c) in the register at address decimal 2 (binary 10)
Store is set to 1

## Slide 14: Storing a value in the RAM
After clock has changed from 0 to 1

## Slide 15: Storing a value in the RAM
I have the data stored in registers and want to read the value stored at register 2 (binary 10)

## Slide 16: Looking at the Logisim RAM component
Logisim RAM with setting:
  Separate load and store ports
To update the memory at an address
  Set the store (str) input to 1
  Set the address and data input
  The memory will change when the clock changes from 0 to 1

## Slide 17: Looking forward
We will connect components together to form an automated device
We have created
  ALU
    Two data inputs
    Input to indicate the operation to carry out
    Output the result of the operation
  Registers
  Counter
  Memory
We will use Logisim built-in components for the registers, counter and memory

## Slide 18: ALU – as created in week 2

## Slide 19: Using the ALU
Use the ALU as a sub-circuit
We can use a register for the output of the ALU

## Slide 20: Using the ALU
Keeping a total
  Connect the register containing the output of the ALU to one of its inputs for the next operation – this register is now an accumulator

## Slide 21: Using the ALU
For this demo we will use an input pin for the second input to the ALU

## Slide 22: What is a program?
A program is a set of instructions
For this ALU an instruction is a number between 0 and 3 (2 bits)
We can use ROM to store the instructions
  Each item in memory has an address
  The number of items we can store depends on the number of bits in the address
  We will use an address of 4 bits

## Slide 23: Feeding an instruction into the ALU
We can store instructions in order in a ROM

## Slide 24: Stepping through the instructions
To run the program
  Get an instruction from ROM and feed to operation of the ALU
  Get next instruction
    Use a counter

## Slide 25: Planning a program
Suppose the program we want to run is
  Add 12
  Subtract 2
  Multiply by 4
ALU OP value | Short format | Output
0 | ADD | The result of adding A and B together
1 | AND | The result of a bitwise A AND B
2 | SUB | The result of subtracting 1 from A
3 | LEFT | The result of shifting the bits in A left by one bit so that the rightmost bit will be filled with a zero.

## Slide 26: Setting up a program
Store our fixed number in the input pin – decimal 12
  That is binary 00001100
ALU OP value | Short format
0 | ADD
1 | AND
2 | SUB
3 | LEFT
I
nstruction
Operation
E
xpected
result
(decimal)
Expected result
(hex)
A
dd 12
0
12
c
S
ubtract
1
2
11
b
S
ubtract
1
2
10
a
Left shift
3
20
14
Left shift
3
40
28

## Slide 27: Setting up the simulation
The second input and the program are set up
One instruction will run each time the clock goes to 1

## Slide 28: Running the program

## Slide 29: Summary
We have looked at a counter and updating addressable memory
We have looked at how we could connect components together to create a device that can automatically carry out a list of instructions
  You should build this automated device in the first part of your lab
    There are instructions for a different program to plan and test
  Remember that, even when we are using Logisim built-in components, we have built equivalents from basic logic gates
  The complex behaviour of a running program is all built from simple parts.