## Slide 1: Computer Architecture
Lectorial Week 5

## Slide 2: Objectives
Looking at last week’s reinforcement exercises
  Improving the machine
  Little Man Computer (LMC)
Making links
Looking forward
  Moving from LMC to MIPS architecture

## Slide 3: Improving the machine
The “computer” developed in the lab sessions had many limitations

## Slide 4: Extending the operations
The instructions will now be 16 bits containing
  The operation for the ALU and the second input to the ALU (when needed)
15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
ALU operation |  | Unused (00) |  | Unused (0000) |  |  |  | Immediate value to use as input |  |  |  |  |  |  | 
Hex digit |  |  |  | Hex digit |  |  |  | Hex digit |  |  |  | Hex digit |  |  | 
ALU operation
-
decimal
Operation
description
ALU operation
-
binary
New format
Hex
0
Add
00
0000
0
1
AND
01
0100
4
2
Subtract 1
10
1000
8
3
Left shift
11
1100
c

## Slide 5: New version of the CPU
The ROM now holds 16 bits at each address

## Slide 6: Preparing the program
The ROM and accumulator show the data in hex but some parts might be easier to work out in binary
Working out the AND
Decimal 27 is binary 0001 1011
Decimal 60 is binary 0011 1100
After a bitwise AND 0001 1000
Program
counter
Operation
(decimal)
Instruction in binary
Instruction
in hex
Expected
value in
accumulator
(binary)
Expected
value in
accumulator
(hex)
0
Add 27
0000 0000 0001 1011
001b
0001 1011
1b
1
AND with 60
0100 0000 0011 1100
403c
0001 1000
18
2
Subtract 1
1000 0000 0000 0000
8000
0001 0111
17
3
Left shift
1100 0000 0000 0000
c000
0010 1110
2e

## Slide 7: Running the program
One instruction will run each time the clock goes to 1

## Slide 8: Running the program
End of simulation when all the instructions have been run

## Slide 9: Little Man Computer

## Slide 10: Little man computer
Machine code
  The numeric format of instructions to be loaded into the mailboxes to run
  Instructions run one after another in order
    … unless some special instructions alter this flow
Assembly language
  Write program using mnemonics and symbols for human readability
  We use labels (words) to represent mailbox numbers
Assembler
  Program that converts Assembly language into machine code
Mnemonic | Name | Op Code
INP | INPUT | 901
OUT | OUTPUT | 902
LDA | LOAD | 5xx
STA | STORE | 3xx
ADD | ADD | 1xx
SUB | SUBTRACT | 2xx
BRP | BRANCH IF POSITIVE | 8xx
BRZ | BRANCH IF ZERO | 7xx
BRA | BRANCH ALWAYS | 6xx
HLT | HALT | 000
DAT | DATA LOCATION | 

## Slide 11: Count down from input number to zero
INP
loop OUT
SUB one
BRP loop
HLT
one DAT 1
Take the number form the input basket and store in the calculator display
one is a label that relates to a memory address

## Slide 12: Looking at computer architectures
  With an introduction to MIPS architecture

## Slide 13: Instruction Set
Each processor has its own instruction set
  The full set of operations that have been built into the hardware by combining logic gates into circuits
  As in the Little Man Computer and Logisim CPU simulations, instructions are given as structured numbers in machine code
  There are many common features across different hardware
A program runs by carrying out a list of instructions on hardware
We are using MIPS
  It’s relatively simple and has a simulator (MARS) for educational use to allow us to get a taste of Assembly language programming

## Slide 14: CISC and RISC
RISC
  Reduced instruction set computing
  Hardware itself is quite simple, smaller instruction set
  Several machine code instructions may be needed for a complex task
  Each instruction takes a single clock cycle
CICS
  Complex instruction set computing
  Larger instruction set
  Complex instructions available directly in the hardware
  Single machine code instruction for complex operations, but may take multiple clock cycles

## Slide 15: Intel x86 family
  Started in 1978 with Intel 8086 (16-bit)
  Currently on Core i9
  Used in most Laptops, Desktops, and Servers
  Backwards Compatible
  Latest versions transitioned to x86-64 Instruction
  CISC

## Slide 16: ARM Processors
Originally for Personal Computers
Most common use in low power devices
Used in smart phones, Raspberry Pi
32 or 64 bit
RISC

## Slide 17: IBM Z Series
CISC
Specialist hardware for business computing – particularly finance
Known as a mainframe

## Slide 18: MIPS
RISC
Influenced other Architectures (ARM)
Used in Embedded Processor in Routers, etc
Used by many Computer Organization type courses
  Used in this Course (MARS simulator)
Instruction set is typical of many modern ISAs

## Slide 19: MIPS Architecture overview
Similar to coursework Logisim CPU
Arithmetic and Logic Unit (ALU)
Instruction Memory
  Machine code
Data Memory
  Memory shown separate for convenience only
Program Counter (PC)
  Address of next instruction to execute

## Slide 20: MIPS Architecture overview continued
Differences from coursework Logisim CPU
Registers
  Fast temporary storage in CPU
  MIPS has 32 registers each holding 32 bits
  In MIPS, the ALU only takes input from registers (not from data memory)

## Slide 21: MIPS Control
Showing detail of how signals are combined and selected

## Slide 22: MIPS Instructions
MIPS instructions are 32 bits
Different Instructions will use those 32 bits in different ways to specify different information
We will have a brief look at one instruction in machine code, but we will write our programs in MIPS assembly language

## Slide 23: MIPS add instruction
add $t0, $s1, $s2
special
$s1
$s2
$t0
0
add
0
17
18
8
0
32
000000
10001
10010
01000
00000
100000
000000100011001001000000001000002 = 0232402016
op
rs
rt
rd
shamt
funct
6 bits
6 bits
5 bits
5 bits
5 bits
5 bits

## Slide 24: MIPS Assembly language
Assembly languages
  Use mnemonics (short written forms of instruction)
  Use human readable labels to identify memory locations
  Needs to be assembled to convert to machine code
MIPS assembly language
  Registers are referred to with a $
  Basic instructions relate directly to the architecture of the hardware
  Extended (pseudo) instructions are converted by the assembler into basic instructions

## Slide 25: Assemblers
Machine code is binary and difficult for humans to read or write
An Assembler translates an Assembly language instruction into the equivalent binary machine code
add $t0, $s1, $s2
000000100011001001000000001000002
Assembly Code
Machine Code

## Slide 26: Looking at an instruction
Instructions in assembly language have a regular format
  First a mnemonic for the operation followed by parameters
  Usually (but not always) the destination is next, then source
add $t0, $t1, $t2
addi $t0, $t1, 1
Operation
Operands (variables, arguments, etc.)
Source Operands (input to the operation)
Destination Operand (where to store result)
Immediate Operand

## Slide 27: MIPS Registers
There are 32 registers
  Each holds 32 bits
  26 general registers, others have specific uses
  Register names start with $ in MIPS Assembly language
The inputs to the ALU are registers
  This means to operate on a variables in memory you must:
    Load the value/values from memory into a register
    Perform the instruction
    Store the result back into memory
  Going to and from memory can be expensive
    (4x to 20x slower than operating on a register)

## Slide 28: Summary
We will write programs in MIPS Assembly language
  We use a small set of instructions
  Arithmetic operations only act on registers
  We have to assemble our programs to turn them into machine code to run them
  We use labels to refer to memory addresses
We use the MARS MIPS Assembler and Runtime Simulator
  Educational environment to simulate a MIPS processor
  We use aspects of Assembly language that are common to many processors
  The simulator allows us to see register contents and step through programs
  Download from
  https://courses.missouristate.edu/KenVollmar/mars/download.htm