## Slide 1: Computer Architecture Concepts
Part 19 – Jumps and Subroutines

## Slide 2: Objectives
Look at how jump instructions can be used to allow subroutines in MIPS Assembly language

## Slide 3: Jump
So far, our programs run each instruction in sequential order until the end of the program
Program counter (PC) stores address of instruction to execute next
  Default move to next instruction in sequence
Jump allows us to move control to another part of the program by explicitly setting the PC to a particular address
  We use a label in Assembly language to specify an address
  Remember a label is just an alias for a memory address

## Slide 4: Subroutines
Similar to procedures / methods in High level languages
Allow Blocks of code/functionality to be reused
  Might need to call the same subroutine in multiple places
  Putting code into subroutine means only one location to maintain/update
  Makes code easier to read

## Slide 5: Subroutine
Program control needs to jump to start of subroutine
  Use a label for the subroutine
When the code in the subroutine has finished control needs to go back to where it would have been
  Return address stored in a register ($ra)

## Slide 6: Jump Instructions
Jump and link (jal)
  Store the program counter in register $ra
  Jump to statement at address given by label
  Example, if printHeader is a label in the .text part of program
  jal printHeader
To return we use jump register (jr) to jump to address given in register
  jr $ra

## Slide 7: Using a subroutine in a program
We want the code in the subroutine to only run when we jump to it with a jal instruction
We must make sure that the program will finish and not run the subroutine code again at the end
Use syscall number 10 to exit a program.

## Slide 8: Example – what does it do?
.data
message: .asciiz "\nLetter "
.text
addi $s0, $zero, 'a'
jal outputMessage
jal outputChar
addi $s0, $s0, 1
jal outputMessage
jal outputChar
addi $v0, $zero, 10
syscall
outputMessage:
la $a0, message
addi $v0, $zero, 4
syscall
jr $ra
outputChar:
addi $v0, $zero, 11
add $a0, $zero, $s0
syscall
jr $ra

## Slide 9: Summary
We have looked at the simplest subroutines in MIPS
  Use jal with a label to jump to the subroutine
    It will automatically store the return address in register $ra
  Use jr with a register to return to the address in that register
  Use syscall 10 to exit the program so that the subroutine doesn’t run again
We have not looked at
  Passing parameters to a subroutine
  Allowing a subroutine to call another subroutine